## Slide 1
计算机系统结构实验课
JSI
Slides taken (with permission) from:
  Derek Chiou (UT Austin)
  Arvind and collaborators (MIT)

## Slide 2: Outlines
Introduction
Bluespec: Combinational Circuits
Bluespec: Sequential Circuits
Practices:
  1: Right Shifter (Gate Primitives)
  2: Right Shifter (Pipelined)
  3: SMIPS Microprocessor (Unpipelined)
  4: SMIPS Microprocessor (Pipelined)

## Slide 3: Outlines
Introduction
Bluespec: Combinational Circuits
Bluespec: Sequential Circuits
Practices:
  1: Right Shifter (Gate Primitives)
  2: Right Shifter (Pipelined)
  3: SMIPS Microprocessor (Unpipelined)
  4: SMIPS Microprocessor (Pipelined)

## Slide 4: What is Bluespec?
A hardware design environment
  A language(Bluespec System Verilog)
  A workstation
  A compiler
  A simulator

## Slide 5: Practice Environment
Lab Server:
  IP Address: 123.56.146.28
  Port: 5126
  Username: your student ID (e.g., SY1906310)
  Password: your student ID (e.g., SY1906310)
  Change the password after you login in.
Note that Your account is created temporarily and shall be deleted at the end of this course, so don’t leave important data there.

## Slide 6: Practice Materials
Lab Docs (/home/bluespec/lab_docs)
Slides (/home/bluespec/slides)

## Slide 7: License Server
Open file ~/.bashrc
Set the Environment Variable
export BLUESPEC_HOME=/tools/bluespec
export BLUESPECDIR=$BLUESPEC_HOME/lib
export PATH=$PATH:$BLUESPEC_HOME/bin
export LM_LICENSE_FILE=/home/bluespec/license/Bluespec_20200428.lic
source ~/.bashrc

## Slide 8: HOWTO
1. Copy the lab_template folder to your own dir.
[SY1906310@cu07 ~]$ cp –r /home/bluespec/lab_template/ ./
2. Untar the Lab.tgz files (Lab1 as an example).
[SY1906310@cu07 ~]$ cd lab_template/
[SY1906310@cu07 lab_template]$ tar -xvf Lab1.tgz
3. Enter the directory and run the spec file.
[SY1906310@cu07 lab_template]$ cd Lab1/
[SY1906310@cu07 Lab1]$ bluespec Lab1.bspec

## Slide 9: Lab1 Example

## Slide 10: Lab1 Example

## Slide 11: Outlines
Introduction
Bluespec: Combinational Circuits
Bluespec: Sequential Circuits
Practices:
  1: Right Shifter (Gate Primitives)
  2: Right Shifter (Pipelined)
  3: SMIPS Microprocessor (Unpipelined)
  4: SMIPS Microprocessor (Pipelined)

## Slide 12: Content
Design of a combinational ALU starting with primitive gates And, Or and Not
Combinational circuits as acyclic wiring diagrams of primitive gates
Introduction to BSV
  Intro to types – enum, typedefs, numeric types, int#(32) vs integer, bool vs bit#(1), vectors
  Simple operations: concatenation, conditionals, loops
  Functions
  Static elaboration and a structural interpretation of the textual code

## Slide 13: Combinational circuits are acyclic interconnections of gates
And, Or, Not
Nand, Nor, Xor
…

## Slide 14: Simple combinational circuits:
Ripple-carry Adder

## Slide 15: Full Adder: A one-bit adder
function fa(a, b, c_in);
s = (a ^ b)^ c_in;
c_out = (a & b) | (c_in & (a ^ b));
return {c_out,s};
endfunction
Structural code – only specifies interconnection between boxes
Not quite correct –needs type annotations

## Slide 16: Full Adder: A one-bit adder corrected
function Bit#(2) fa(Bit#(1) a, Bit#(1) b,
Bit#(1) c_in);
Bit#(1) s = (a ^ b)^ c_in;
Bit#(1) c_out = (a & b) | (c_in & (a ^ b));
return {c_out,s};
endfunction
“Bit#(1) a” type declaration says that a is one bit wide
{c_out,s} represents bit concatenation
How big is {c_out,s}?
2 bits

## Slide 17: Types
A type is a grouping of values
  Integer: 1, 2, 3, …
  Bool: True, False
  Bit: 0,1
  A pair of Integers: Tuple2#(Integer, Integer)
  A function fname from Integers to Integers:
  function Integer fname (Integer arg)
Every expression and variable in a Bluespec program has a type; sometimes it is specified explicitly and sometimes it is deduced by the compiler
Thus we say an expression has a type or belongs to a type
Each expression has a unique type

## Slide 18: Type declaration versus deduction
The programmer writes down types of some expressions in a program and the compiler deduces the types of the rest of expressions
If the type deduction cannot be performed or the type declarations are inconsistent then the compiler complains
function Bit#(2) fa(Bit#(1) a, Bit#(1) b,
Bit#(1) c_in);
Bit#(1) s = (a ^ b)^ c_in;
Bit#(2) c_out = (a & b) | (c_in & (a ^ b));
return {c_out,s};
endfunction
type error
Type checking prevents lots of silly mistakes

## Slide 19: 2-bit Ripple-Carry Adder
function Bit#(3) add(Bit#(2) x, Bit#(2) y,
Bit#(1) c0);
Bit#(2) s = 0; Bit#(3) c=0; c[0] = c0;
let cs0 = fa(x[0], y[0], c[0]);
c[1] = cs0[1]; s[0] = cs0[0];
let cs1 = fa(x[1], y[1], c[1]);
c[2] = cs1[1]; s[1] = cs1[0];
return {c[2],s};
endfunction
fa
fa
x[0]
y[0]
c[0]
s[0]
x[1]
y[1]
c[1]
s[1]
c[2]
Fa can be used as a black box as long as we understand its type signature and its function
The “let” syntax avoids having to write down types explicitly

## Slide 20: “let” syntax
The “let” syntax: asks compiler to infer type
  avoids having to write down types explicitly
  let cs0 = fa(x[0], y[0], c[0]);
  Bits#(2) cs0 = fa(x[0], y[0], c[0]);
The same

## Slide 21: Parameterized types: #
A type declaration itself can be parameterized by other types
Parameters are indicated by using the syntax ‘#’
  For example Bit#(n) represents n bits and can be instantiated by specifying a value of n
  Bit#(1), Bit#(32), Bit#(8), …

## Slide 22: An w-bit Ripple-Carry Adder
function Bit#(w+1) addN(Bit#(w) x, Bit#(w) y,
Bit#(1) c0);
Bit#(w) s; Bit#(w+1) c=0; c[0] = c0;
for(Integer i=0; i<w; i=i+1)
begin
let cs = fa(x[i],y[i],c[i]);
c[i+1] = cs[1]; s[i] = cs[0];
end
return {c[w],s};
endfunction
Not quite correct
Unfold the loop to get the wiring diagram
fa
fa
x[0]
y[0]
c[0]
s[0]
x[1]
y[1]
c[1]
s[1]
c[2]
cs
fa
x[w-1]
y[w-1]
s[w-1]
c[w]
c[w-1]
…

## Slide 23: Instantiating the parametric Adder
function Bit#(w+1) addN(Bit#(w) x, Bit#(w) y,
Bit#(1) c0);
// concrete instances of addN!
function Bit#(33) add32(Bit#(32) x, Bit#(32) y,
Bit#(1) c0) = addN(x,y,c0);
function Bit#(4) add3(Bit#(3) x, Bit#(3) y,
Bit#(1) c0) = addN(x,y,c0);
Define add32, add3 … using addN

## Slide 24: valueOf(w) versus w
Each expression has a type and a value and these come from two entirely disjoint worlds
w in Bit#(w) resides in the types world
Sometimes we need to use values from the types world into actual computation. The function valueOf allows us to do that
  Thus
  i<w is not type correct
  i<valueOf(w)is type correct

## Slide 25: TAdd#(w,1) versus w+1
Sometimes we need to perform operations in the types world that are very similar to the operations in the value world
  Examples: Add, Mul, Log
We define a few special operators in the types world for such operations
  Examples: TAdd#(m,n), TMul#(m,n), …

## Slide 26: A w-bit Ripple-Carry Adder corrected
function Bit#(TAdd#(w,1)) addN(Bit#(w) x, Bit#(w) y,
Bit#(1) c0);
Bit#(w) s; Bit#(TAdd#(w,1)) c=0; c[0] = c0;
let valw = valueOf(w);
for(Integer i=0; i<valw; i=i+1)
begin
let cs = fa(x[i],y[i],c[i]);
c[i+1] = cs[1]; s[i] = cs[0];
end
return {c[valw],s};
endfunction

## Slide 27: A w-bit Ripple-Carry Adder
function Bit#(TAdd#(w,1)) addN(Bit#(w) x, Bit#(w) y,
Bit#(1) c0);
Bit#(w) s; Bit#(TAdd#(w,1)) c; c[0] = c0;
let valw = valueOf(w);
for(Integer i=0; i<valw; i=i+1)
begin
let cs = fa(x[i],y[i],c[i]);
c[i+1] = cs[1]; s[i] = cs[0];
end
return {c[valw],s};
endfunction
types world
equivalent of w+1
Lifting a type into the value world
Structural interpretation of a loop – unfold it to generate an acyclic graph

## Slide 28: Static Elaboration phase
When Bluespec program are compiled, type checking is done first. Then the compiler eliminates many constructs which have no direct hardware meaning, like Integers, loops
cs0 = fa(x[0], y[0], c[0]); c[1]=cs0[1]; s[0]=cs0[0];
cs1 = fa(x[1], y[1], c[1]); c[2]=cs1[1]; s[1]=cs1[0];
…
csw = fa(x[valw-1], y[valw-1], c[valw-1]);
c[valw] = csw[1]; s[valw-1] = csw[0];
for(Integer i=0; i<valw; i=i+1) begin
let cs = fa(x[i],y[i],c[i]);
c[i+1] = cs[1]; s[i] = cs[0];
end

## Slide 29: Integer versus Int#(32)
In mathematics integers are unbounded but in computer systems integers always have a fixed size
Bluespec allows us to express both types of integers, though unbounded integers are used only as a programming convenience
for(Integer i=0; i<valw; i=i+1)
begin
let cs = fa(x[i],y[i],c[i]);
c[i+1] = cs[1]; s[i] = cs[0];
end

## Slide 30: Type synonyms
typedef bit [7:0] Byte;
typedef Bit#(8) Byte;
typedef Bit#(32) Word;
typedef Tuple2#(a,a) Pair#(type a);
typedef Int#(n) MyInt#(type n);
typedef Int#(n) MyInt#(numeric type n);
The same
The same
Notes: Define MyInt

## Slide 31: Arithmetic-Logic Unit (ALU)
ALU performs all the arithmetic and logical functions
Op
- Add, Sub, ...
- And, Or, Xor, Not, ...
- GT, LT, EQ, Zero, ...
Result
Comp?
A
B
ALU
We first implement individual functions like Add and then combine them to form an ALU

## Slide 32: Shift operators

## Slide 33: Logical right shift by 2
0
0
Fixed size shift operation is cheap in hardware – just wire the circuit appropriately
Rotate, sign-extended shifts – all are equally easy
a b c d
0 0 a b

## Slide 34: Conditional operation: shift versus no-shift
We need a mux to select the appropriate wires: if s is one the mux will select the wires on the left otherwise it would select wires on the right
s
(s==0)?{a,b,c,d}:{0,0,a,b};
0
0

## Slide 35: A 2-way multiplexer
(s==0)?A:B
A
B
S
AND
AND
OR
S
A
B
Gate-level implementation
We will use conditional expressions which will be synthesized using muxes

## Slide 36: A 4-way multiplexer
case {s1,s0} matches
0: A;
1: B;
2: C;
3: D;
endcase
S0
S0
S1
A
B
C
D

## Slide 37: Logical right shift by n
Shift n can be broken down in log n steps of fixed-length shifts of size 1, 2, 4, …
  Shift 3 can be performed by doing a shift 2 and shift 1
We need a mux to omit a particular size shift
Shift circuit can be expressed as log n nested conditional expressions
You will write a Blusepec program to produce a variable size shifter in Lab 1
0
0
0
s0
s1

## Slide 38: A Degression on Types
Suppose we have a variable c whose values can represent three different colors
  We can declare the type of c to be Bit#(2) and say that 00 represents Red, 01 Blue and 10 Green
A better way is to create a new type called Color as follows:
typedef enum {Red, Blue, Green}
Color deriving(Bits, Eq);
The compiler will automatically assign some bit representation to the three colors and also provide a function to test if two colors are equal. If you do not use “deriving” then you will have to specify the representation and equality
Types prevent us from mixing raw bits and bits that represent color

## Slide 39: Enumerated types
typedef enum {Red, Blue, Green}
Color deriving(Bits, Eq);
typedef enum {Eq, Neq, Le, Lt, Ge, Gt, AT, NT}
BrFunc deriving(Bits, Eq);
typedef enum {Add, Sub, And, Or, Xor, Nor, Slt, Sltu, LShift, RShift, Sra}
AluFunc deriving(Bits, Eq);
Each enumerated type defines a new type
Notes: Can same text be in 2 enumerated types?

## Slide 40: Combinational ALU
function Data alu(Data a, Data b, AluFunc func);
Data res = case(func)
Add : (a + b);
Sub : (a - b);
And : (a & b);
Or : (a | b);
Xor : (a ^ b);
Nor : ~(a | b);
Slt : zeroExtend( pack( signedLT(a, b) ) );
Sltu : zeroExtend( pack( a < b ) );
LShift: (a << b[4:0]);
RShift: (a >> b[4:0]);
Sra : signedShiftRight(a, b[4:0]);
endcase;
return res;
endfunction
Given an implementation of the primitive operations like addN, Shift, etc. the ALU can be implemented simply by introducing a mux controlled by op to select the appropriate circuit

## Slide 41: Comparison operators
function Bool aluBr(Data a, Data b, BrFunc brFunc);
Bool brTaken = case(brFunc)
Eq : (a == b);
Neq : (a != b);
Le : signedLE(a, 0);
Lt : signedLT(a, 0);
Ge : signedGE(a, 0);
Gt : signedGT(a, 0);
AT : True;
NT : False;
endcase;
return brTaken;
endfunction
Notes: 41

## Slide 42: ALU including Comparison operators
mux
a
func
…
mux
brFunc
Add
LShift
Eq
…
b

## Slide 43: Complex combinational circuits
Multiplication

## Slide 44: Multiplication by repeated addition
1101 (13)
1011 (11)
1101
+ 1101
+ 0000
+ 1101
10001111 (143)
b Multiplicand
a Muliplier *
add4
add4
add4
a0
a1
a2
a3
m0
m1
m2
m3
0
mi = (a[i]==0)? 0 : b;

## Slide 45: Combinational 32-bit multiply
function Bit#(64) mul32(Bit#(32) a, Bit#(32) b);
Bit#(32) prod = 0; Bit#(32) tp = 0; for(Integer i = 0; i < 32; i = i+1) begin Bit#(32) m = (a[i]==0)? 0 : b; Bit#(33) sum = add32(m,tp,0); prod[i] = sum[0]; tp = truncateLSB(sum); end return {tp,prod}; endfunction

## Slide 46: Design issues with combinational multiply
Lot of hardware
  32-bit multiply uses 31 add32 circuits
Long chains of gates
  32-bit ripple carry adder has a 31-long chain of gates
  32-bit multiply has 31 ripple carry adders in sequence!
The speed of a combinational circuit is determined by its longest input-to-output path
Can we do better?

## Slide 47: What Did We Learn?
Combinational circuits in Bluespec
  Add, shift, multiply
Bluespec Types
  Parameterized
  valueOf
  Tadd#
  Integer vs Int#
  Enumerated Types
Static Elaboration

## Slide 48: Outlines
Introduction
Bluespec: Combinational Circuits
Bluespec: Sequential Circuits
Practices:
  1: Right Shifter (Gate Primitives)
  2: Right Shifter (Pipelined)
  3: SMIPS Microprocessor (Unpipelined)
  4: SMIPS Microprocessor (Pipelined)

## Slide 49: Content
Introduce sequential circuits as a way of saving area
  Edge-triggered Flip-flop
  Register
New Bluespec concepts
  state elements
  rules and actions for describing dynamic behavior
  modules and methods

## Slide 50: Combinational 32-bit multiply
function Bit#(64) mul32(Bit#(32) a, Bit#(32) b);
Bit#(32) prod = 0; Bit#(32) tp = 0; for(Integer i = 0; i < 32; i = i+1) begin Bit#(32) m = (a[i]==0)? 0 : b; Bit#(33) sum = add32(m,tp,0); prod[i] = sum[0]; tp = truncateLSB(sum); end return {tp,prod}; endfunction
Combinational circuit uses 31 add32 circuits
We can reuse the same add32 circuit if we can store the partial results in some storage device, e.g., register

## Slide 51: Combinational circuits
OpSelect
- Add, Sub, ...
- And, Or, Xor, Not, ...
- GT, LT, EQ, Zero, ...
Result
Comp?
A
B
ALU
Sel
O
A0
A1
An-1
Mux
.
.
.
lg(n)
Sel
O0
O1
On-1
A
Demux
.
.
.
lg(n)
A
Decoder
.
.
.
O0
O1
On-1
lg(n)
Such circuits have no cycles (feedback) or state elements

## Slide 52: A simple synchronous state element
ff
Q
D
C
C
D
Q
Metastability possible if data available too late
Data is sampled at the rising edge of the clock
Edge-Triggered Flip-flop

## Slide 53: Flip-flops with Write Enables
ff
Q
D
C
EN
C
D
Q
EN
ff
Q
D
C
EN
0
1
ff
Q
D
C
EN
dangerous!
Data is captured only if EN is on
Notes: Why dangerous?
Glitches

## Slide 54: Registers
Register: A group of flip-flops with a common
clock and enable
Register file: A group of registers with a common
clock, input and output port(s)
ff
D
ff
D
ff
D
ff
D
ff
D
ff
D
ff
D
ff
Q
Q
Q
Q
Q
Q
Q
Q
D
C
En

## Slide 55: Register Files
ReadData1
ReadSel1
ReadSel2
WriteSel
Register
file
2R + 1W
ReadData2
WriteData
WE
Clock
Reads are combinational and not affected by the write until the next clock cycle
register 1
WSel
C
register 0
WData
WE
RSel2
RData2
RSel1
RData1

## Slide 56: Register Files and Ports
Ports are expensive multiplex single port for read & write
ReadData1
ReadSel1
ReadSel2
WriteSel
Register
file
2R + 1W
ReadData2
WriteData
WE
ReadData
ReadSel
R/WSel
Register
file
1R + 1R/W
R/WData
WE

## Slide 57: We can build useful and compact circuits using registers
Circuits containing state elements are called sequential circuits

## Slide 58: Expressing a loop using registers
int s = s0;
for (int i = 0; i < 32; i = i+1) { s = f(s); } return s; C-code
sel
< 32
0
notDone
+1
i
en
sel = start
en = start | notDone
s0
f
sel
s
en
We need two registers to hold s and i values from one iteration to the next.
These registers are initialized when the computation starts and updated every cycle until the computation terminates

## Slide 59: Expressing sequential circuits in Bluespec
Sequential circuits, unlike combinational circuits, are not expressed structurally (as wiring diagrams) in Bluespec
For sequential circuits a designer defines:
  State elements by instantiating modules
Reg#(Bit#(32)) s <- mkRegU();
Reg#(Bit#(6)) i <- mkReg(32);
  Rules which define how state is to be transformed atomically
  rule step if (i < 32); s <= f(s); i <= i+1; endrule
make a 32-bit register which is uninitialized
make a 6-bit register with initial value 32
the rule can execute only when its guard is true
actions to be performed when the rule executes

## Slide 60: Rule Execution
< 32
notDone
+1
sel
0
i
en
sel = start
en = start | notDone
f
s0
sel
s
en
Reg#(Bit#(32)) s <- mkRegU();
Reg#(Bit#(6)) i <- mkReg(32);
rule step if (i < 32); s <= f(s); i <= i+1; endrule
When a rule executes:
  all the registers are read at the beginning of a clock cycle
  the guard and computations to evaluate the next value of the registers are performed
  at the end of the clock cycle registers are updated if the guard is true
Muxes are need to initialize the registers

## Slide 61: Multiply using registers
function Bit#(64) mul32(Bit#(32) a, Bit#(32) b);
Bit#(32) prod = 0; Bit#(32) tp = 0; for(Integer i = 0; i < 32; i = i+1) begin Bit#(32) m = (a[i]==0)? 0 : b; Bit#(33) sum = add32(m,tp,0); prod[i] = sum[0]; tp = truncateLSB(sum); end return {tp,prod}; endfunction
Need registers to hold a, b, tp, prod and i
Update the registers every cycle until we are done
Combinational version

## Slide 62: Sequential multiply
Reg#(Bit#(32)) a <- mkRegU();
Reg#(Bit#(32)) b <- mkRegU();
Reg#(Bit#(32)) prod <-mkRegU(); Reg#(Bit#(32)) tp <- mkRegU();
Reg#(Bit#(6)) i <- mkReg(32);
rule mulStep if (i < 32); Bit#(32) m = (a[i]==0)? 0 : b; Bit#(33) sum = add32(m,tp,0); prod[i] <= sum[0]; tp <= sum[32:1];
i <= i+1; endrule
state elements
a rule to describe the dynamic behavior
The rule won’t fire until i is set to value smaller than 32
similar to the loop body in the combinational version
Notes: Need to provide values to a and b at some point.

## Slide 63: Dynamic selection requires a mux
a[i]
a
i
a[0],a[1],a[2],…
a
>>
0
when the selection indices are regular then it is better to use a shift operator (no gates!)

## Slide 64: Replacing repeated selections by shifts
Reg#(Bit#(32)) a <- mkRegU();
Reg#(Bit#(32)) b <- mkRegU();
Reg#(Bit#(32)) prod <-mkRegU(); Reg#(Bit#(32)) tp <- mkRegU();
Reg#(Bit#(6)) i <- mkReg(32);
rule mulStep if (i < 32); Bit#(32) m = (a[0]==0)? 0 : b;
a <= (a >> 1); Bit#(33) sum = add32(m,tp,0); prod <= {sum[0], (prod >> 1)[30:0]}; tp <= sum[32:1];
i <= i+1; endrule

## Slide 65: Circuit for Sequential Multiply
bIn
b
a
i
== 32
0
done
+1
prod
result (low)
<<
[30:0]
aIn
<<
31:0
tp
s1
s1
s1
s2
s2
s2
s2
s1
s1 = start_en
s2 = start_en | !done
result (high)
31
0
add
0
0
32:1
0

## Slide 66: Circuit analysis
Number of add32 circuits has been reduced from 31 to one, though some registers and muxes have been added
The longest combinational path has been reduced from 31 serial add32’s to one add32 plus a few muxes
The sequential circuit will take 31 clock cycles to compute an answer

## Slide 67: Modules
We often package sequential circuits into modules to hide the details

## Slide 68: Multiply Module
rdy
en
Bit#(32)
Bit#(64)
rdy
start
result
Multiply
module
Bit#(32)
interface Multiply;
method Action start
(Bit#(32) a, Bit#(32) b);
method Bit#(64) result();
endinterface
A module in Bluespec is like an object in an object-oriented language and can only be manipulated via the methods of its interface
However, unlike software, a method in Bluespec can be applied only when it is “ready”
Furthermore, application of an action method, i.e., a method that changes the state of a module, is indicated by asserting the associated enable wire

## Slide 69: Multiply Module
module mkMultiply32 (Multiply);
Reg#(Bit#(32)) a <- mkRegU();
Reg#(Bit#(32)) b <- mkRegU();
Reg#(Bit#(32)) prod <-mkRegU(); Reg#(Bit#(32)) tp <- mkRegU();
Reg#(Bit#(6)) i <- mkReg(32);
rule mulStep if (i != 32);
Bit#(32) m = (a[0]==0)? 0 : b; Bit#(33) sum = add32(m,tp,0); prod <= {sum[0], (prod >> 1)[30:0]}; tp <= truncateLSB(sum); a <= a >> 1; i <= i+1;
endrule
method Action start(Bit#(32) aIn, Bit#(32) bIn)
if (i == 32);
a <= aIn; b <= bIn; i <= 0; tp <= 0; prod <= 0;
endmethod
method Bit#(64) result() if (i == 32);
return {tp,prod};
endmethod endmodule
State
Internal
behavior
External
interface
method guards

## Slide 70: Module: Method Interface
s1 = start_en
s2 = start_en | !done
== 32
0
done
+1
aIn
bIn
en
rdy
result
rdy
start
result
s1
OR
s1
s2
bIn
b
a
i
prod
result (low)
<<
[30:0]
aIn
<<
31:0
tp
result (high)
add
0
31
0
0
s1
s1
s1
s2
s2
s2
s2
s1
32:1
0

## Slide 71: Polymorphic Multiply Module
rdy
en
Bit#(32)
Bit#(64)
rdy
start
result
Multiply
module
Bit#(32)
implicit conditions
interface Multiply;
method Action start (Bit#(32) a, Bit#(32) b);
method Bit#(64) result();
endinterface
n
#(Numeric type n)
n
Tadd(n,n)
n
n
TAdd#(n,n)
n could be
32, 13, …
The module can easily be made polymorphic

## Slide 72: Sequential n-bit multiply
module mkMultiplyN (MultiplyN#(n));
Reg#(Bit#(n)) a <- mkRegU();
Reg#(Bit#(n)) b <- mkRegU();
Reg#(Bit#(n)) prod <-mkRegU(); Reg#(Bit#(n)) tp <- mkRegU();
let nv = fromInteger(valueOf(n)); Reg#(Bit#(TAdd#(TLog#(n),1))) i <- mkReg(nv);
rule mulStep if (i != nv);
Bit#(n) m = (a[0]==0)? 0 : b; Bit#(Tadd#(n,1)) sum = addN(m,tp,0); prod <= {sum[0], (prod >> 1)[(nv-2):0]}; tp <= truncateLSB(sum); a <= a >> 1; i <= i+1;
endrule
method Action start(Bit#(n) aIn, Bit#(n) bIn) if (i == nv);
a <= aIn; b <= bIn; i <= 0; tp <= 0; prod <= 0;
endmethod method Bit#(Tadd#(n,n)) result() if (i == nv);
return {tp,prod};
endmethod endmodule

## Slide 73: Multiply Module
interface Multiply;
method Action start (Bit#(32) a, Bit#(32) b);
method Bit#(64) result();
endinterface
The same interface can be implemented in many different ways:
  module mkMultiply (Multiply)
  module mkBlockMultiply (Multiply)
  module mkBoothMultiply (Multiply)…

## Slide 74: What Did We Learn?
State
Sequential circuits
  Reduce duplication/area at the cost of speed, additional state, and control
How to implement sequential circuits in Bluespec

## Slide 75: Outlines
Introduction
Bluespec: Combinational Circuits
Bluespec: Sequential Circuits
Practices:
  1: Right Shifter (Gate Primitives)
  2: Right Shifter (Pipelined)
  3: SMIPS Microprocessor (Unpipelined)
  4: SMIPS Microprocessor (Pipelined)

## Slide 76: Practice 1 (Lab1.docx)
To build up a right shifter from gate primitives
  First, you will build a simple 1-bit multiplexer
  Next, you will write a simple polymorphic multiplexer using for loops
  Using the gate-level multiplexer function, you will then construct a combinational right-shifter
  Finally, add a simple gate-level modification to the right shifter to support the arithmetic right shift operation

## Slide 77
Files
  RightShifter.bsv(wait to be modified), RightShifterTypes.bsv, Gates.bsv, and RightShifterTest.bsv.
Test
  Use RightShifterTest.bsv to test your code（RightShifter.bsv）
  There are many ways to write tests.

## Slide 78: Practice 2 (Lab2.docx)
This lab is to implement a sequential circuit version of your shifter and a pipelined version of your shifter.
Notes: This lab is to implement a sequential circuit version of your shifter and a pipelined version of your shifter.

## Slide 79
File
  RightShifter.bsv(wait to be modified), RightShifterTypes.bsv, Gates.bsv, and TestShifterPipe.bsv
Test
  Use TestShifterPipe.bsv to test your code（RightShifter.bsv）

## Slide 80: Practice 3 (Lab3.docx part1)
Working with a two stage, unpipelined sequential circuit version of a SMIPS microprocessor
completing the code and adding a third stage (still unpipelined) to the code.
Resolving mispredicted branches

## Slide 81
SMIPS is a simplified MIPS ISA

## Slide 82
Modify a two stages unpipelined sequential circuit version to a third stages unpipelined version

## Slide 83: Practice 4 (Lab3.docx part2)
A two stage pipelined version of the SMIPS processor
You need to modify the code to send the branch resolution to fetch stage, irrespective of whether it's mispredicted or not
On a branch mispredict, change the epoch, to throw away wrong path instructions

## Slide 84
Files
  Part1:/proc/Unpipelined/2cyc_Harvard.bsv
  Part2:/proc/ControlHazardOnly/pcMsg_epoch.bsv
Test
  /proc/ControlHazardOnly/test.bsv

## Slide 85: The MIPS ISA
Processor State
  32 32-bit GPRs, R0 always contains a 0
  PC, the program counter
  some other special registers
Data types
  8-bit byte, 16-bit half word
  32-bit word for integers
Load/Store style instruction set
  data addressing modes- immediate & indexed
  branch addressing modes- PC relative & register indirect
  All instructions are 32 bits
  Byte addressable memory- big endian mode
r0 - r31
PC
Registers
Floating point, memory management and other systems instructions are not includes in the SMIPS subset

## Slide 86: Instruction formats
Only three formats but the fields are used differently by different types of instructions
6 5 5 16
opcode rs rt immediate I-type
6 5 5 5 5 6
opcode rs rt rd shamt func R-type
6 26
opcode target J-type

## Slide 87: Instruction formats cont
Computational Instructions
Load/Store Instructions
opcode rs rt immediate rt  (rs) op immediate
6 5 5 5 5 6
0 rs rt rd 0 func rd  (rs) func (rt)
rs is the base register
rt is the destination of a Load or the source for a Store
6 5 5 16 addressing mode
opcode rs rt displacement (rs) + displacement
31 26 25 21 20 16 15 0

## Slide 88: Control Instructions
Conditional (on GPR) PC-relative branch
  target address = (offset in words)4 + (PC+4)
  range: 128 KB range
Unconditional register-indirect jumps
Unconditional absolute jumps
  target address = {PC<31:28>, target4}
  range : 256 MB range
6 5 5 16
opcode rs offset BEQZ, BNEZ
6 26
opcode target J, JAL
6 5 5 16
opcode rs JR, JALR
  jump-&-link stores PC+4 into the link register (R31)

## Slide 89: Instruction Execution
Execution of an instruction involves
    1. Instruction fetch
    2. Decode
    3. Register fetch
    4. ALU operation
    5. Memory operation (optional)
    6. Write back
and the computation of the next instruction address

## Slide 90: Implementing an ISA
Instruction fetch
  requires an Instruction memory, PC
Decode
  requires understanding the instruction format
Register Fetch
  requires interaction with a register file with a specific number of read/write ports
ALU
  must have the ability to carry out the specified ops
Memory operations
  requires a data memory
Write-back
  requires interaction with the register file
Update the PC
  requires arithmetic ops to calculate pc and condition

## Slide 91: A single-cycle implementation
A single-cycle MIPS implementation requires:
  A register file with 2 read ports and a write port
  An instruction memory, separate from data memory so that we can fetch an instruction as well as perform a data operation (Load/store) on the memory
fetch & execute
pc
iMem
dMem
rf
CPU

## Slide 92: Single-Cycle SMIPS
PC
Inst
Memory
Decode
Register File
Execute
Data
Memory
+4
Datapath is shown only for convenience; it will be derived automatically from the high-level textual description
2 read & 1 write ports
separate Instruction & Data memories
Notes: 92

## Slide 93: Single-Cycle SMIPS
PC
Inst
Memory
Decode
Register File
Execute
Data
Memory
+4
The whole system was described using one rule; lots of big combinational functions
performance?
Notes: 93

## Slide 94: Single-Cycle SMIPS code structure (simplified)
module mkProc(Proc);
Reg#(Addr) pc <- mkRegU;
RFile rf <- mkRFile;
IMemory iMem <- mkIMemory;
DMemory dMem <- mkDMemory;
rule doProc(Cop.started);
let inst = iMem.req(pc);
let dInst = decode(inst);
let rVal1 = rf.rd1(validRegValue(dInst.rSrc1));
let rVal2 = rf.rd2(validRegValue(dInst.rSrc2));
let eInst = exec(dInst, rVal1, rVal2, pc, ?);
update rf, pc and dMem
Notes: 94

## Slide 95: Decoding Instructions: extract fields needed for execution from each instruction
immValid
instruction
branchComp
rDst
rSrc1
rSrc2
imm
ext
aluFunc
instType
31:26
31:26
5:0
31:26
20:16
15:11
25:21
20:16
15:0
25:0
Lot of pure combinational logic: will be derived automatically from the high-level description
decode
Not all fields are defined for every instruction
Notes: 95

## Slide 96: Typedefs
typedef enum {Alu, Ld, St, J, Jr, Jal, Jalr, Br}
IType deriving(Bits, Eq);
typedef enum {Eq, Neq, Le, Lt, Ge, Gt, AT, NT}
BrFunc deriving(Bits, Eq);
typedef enum {Add, Sub, And, Or, Xor, Nor, Slt, Sltu,
LShift, RShift, Sra}
AluFunc deriving(Bits, Eq);

## Slide 97: Decoding Instructions: input-output types
decode
instruction
brFunc
rDst
rSrc1
rSrc2
imm
ext
aluFunc
iType
31:26, 5:0
31:26
5:0
31:26
20:16
15:11
25:21
20:16
15:0
25:0
Type DecodedInst
Bit#(32)
IType
AluFunc
Maybe#(FullIndx)
Maybe#(FullIndx)
Maybe#(FullIndx)
BrFunc
Maybe#(Data)
Mux control logic not shown
Notes: 97
Green is type…

## Slide 98: Decode Function
function DecodedInst decode(Bit#(32) inst);
DecodedInst dInst = ?;
let opcode = inst[ 31 : 26 ];
let rs = inst[ 25 : 21 ];
let rt = inst[ 20 : 16 ];
let rd = inst[ 15 : 11 ];
let funct = inst[ 5 : 0 ];
let imm = inst[ 15 : 0 ];
let target = inst[ 25 : 0 ];
case (opcode)
...
endcase
return dInst;
endfunction
initially undefined

## Slide 99: Instruction Encoding
Bit#(6) opADDIU = 6’b001001;
Bit#(6) opSLTI = 6’b001010;
Bit#(6) opLW = 6’b100011;
Bit#(6) opSW = 6’b101011;
Bit#(6) opJ = 6’b000010;
Bit#(6) opBEQ = 6’b000100;
…
Bit#(6) opFUNC = 6’b000000;
Bit#(6) fcADDU = 6’b100001;
Bit#(6) fcAND = 6’b100100;
Bit#(6) fcJR = 6’b001000;
…
Bit#(6) opRT = 6’b000001;
Bit#(6) rtBLTZ = 5’b00000;
Bit#(6) rtBGEZ = 5’b00100;
Notes: Better as enum…

## Slide 100: Decoding ALU Instructions
case (opcode)
opADDIU, opSLTI, opSLTIU, opANDI, …: begin
dInst.iType = Alu;
dInst.aluFunc = case (opcode)
opADDIU, opLUI: Add;
opSLTI: Slt;
…
endcase;
dInst.dst = validReg(rt);
dInst.src1 = validReg(rs);
dInst.src2 = Invalid;
dInst.imm = Valid(case (opcode)
opADDIU, opSLTI, opSLTIU: signExtend(imm);
opLUI: {imm, 16'b0};
default: zeroExtend(imm);
endcase);
dInst.brFunc = NT;
Notes: 100

## Slide 101: Decoding Load Instructions
opLB, opLH, opLW, opLBU, opLHU: begin
dInst.iType = Ld;
dInst.byteEn = replicate(False);
case (opcode)
opLB, opLBU: dInst.byteEn[0] = True;
opLH, opLHU: begin
dInst.byteEn[0] = True;dInst.byteEn[1] = True;
end
opLW: dInst.byteEn = replicate(True);
endcase
…
dInst.aluFunc = Add;
dInst.dst = validReg(rt);
dInst.src1 = validReg(rs); dInst.src2 = Invalid;
dInst.imm = Valid(signExtend(imm));
dInst.brFunc = NT;
end
Notes: 101

## Slide 102: Decoding Jump Instructions
opJ, opJAL:
begin
dInst.iType = J;
dInst.dst = opcode == opJ? Invalid: validReg(31);
dInst.src1 = Invalid;
dInst.src2 = Invalid;
dInst.imm = Valid(zeroExtend({target,2'b00}));
dInst.brFunc = AT;
end
Notes: 102

## Slide 103: Decoding Branch Instructions
opBEQ, opBNE, opBLEZ, opBGTZ, opRT:
begin
dInst.iType = Br;
dInst.brFunc = case(opcode)
opBEQ: Eq;
opBNE: Neq;
opBLEZ: Le;
opBGTZ: Gt;
opRT: (rt==rtBLTZ ? Lt : Ge);
endcase;
dInst.dst = Invalid;
dInst.src1 = validReg(rs);
dInst.src2 = (opcode==opBEQ || opcode==opBNE)? validReg(rt) : Invalid;
dInst.imm = Valid(signExtend(imm) << 2);
end
Notes: 103

## Slide 104: Reading Registers
Read registers
RVal2
RVal1
RF
RSrc2
Pure combinational logic
RSrc1
Notes: 104

## Slide 105: Executing Instructions
execute
dInst
addr
brTaken
data
iType
rDst
ALU
Branch
Address
pc
rVal2
rVal1
Pure combinational logic
either for memory reference or branch target
either for rf write or St
ALUBr
Notes: 105
ALU should be split…

## Slide 106: Some Useful Functions
function Maybe#(FullIndx) validReg(RIndx idx) = Valid (FullIndx{regType: Normal, idx: idx});
function Maybe#(FullIndx) validCop(RIndx idx) = Valid (FullIndx{regType: CopReg, idx: idx});
function RIndx validRegValue(Maybe#(FullIndx) idx) = validValue(idx).idx;

## Slide 107: Execute Function
function ExecInst exec(DecodedInst dInst, Data rVal1, Data rVal2, Addr pc, Addr ppc, Data copVal);
ExecInst eInst = ?;
Data aluVal2 = isValid(dInst.imm) ? validValue(dInst.imm) : rVal2;
let aluRes = alu(rVal1, aluVal2, dInst.aluFunc);
eInst.iType = dInst.iType;
eInst.data = dInst.iType == Mfc0? copVal :
dInst.iType == Mtc0? rVal1 :
dInst.iType==St? rVal2 :
(dInst.iType==J || dInst.iType==Jr) ?
(pc+4) : aluRes;
eInst.byteEn = dInst.byteEn;
eInst.unsignedLd = dInst.unsignedLd;

## Slide 108: Execute Function (2)
let brTaken = aluBr(rVal1, rVal2, dInst.brFunc);
let brAddr = brAddrCalc(pc, rVal1, dInst.iType, validValue(dInst.imm), brTaken);
eInst.mispredict = brAddr != ppc;
eInst.brTaken = brTaken;
eInst.addr = (dInst.iType == Ld || dInst.iType == St) ? aluRes : brAddr;
eInst.dst = dInst.dst;
return eInst;
endfunction

## Slide 109: ALU
function Data alu(Data a, Data b, AluFunc func);
Data res = case(func)
Add : (a + b);
Sub : (a - b);
And : (a & b);
Or : (a | b);
Xor : (a ^ b);
Nor : ~(a | b);
Slt : zeroExtend( pack( signedLT(a, b) ) );
Sltu : zeroExtend( pack( a < b ) );
LShift: (a << b[4:0]);
RShift: (a >> b[4:0]);
Sra : signedShiftRight(a, b[4:0]);
endcase;
return res;
endfunction
Notes: 109

## Slide 110: Branch Resolution
function Bool aluBr(Data a, Data b, BrFunc brFunc);
Bool brTaken = case(brFunc)
Eq : (a == b);
Neq : (a != b);
Le : signedLE(a, 0);
Lt : signedLT(a, 0);
Ge : signedGE(a, 0);
Gt : signedGT(a, 0);
AT : True;
NT : False;
endcase;
return brTaken;
endfunction
Notes: 110

## Slide 111: Branch Address Calculation
function Addr brAddrCalc(Addr pc, Data val, IType iType, Data imm, Bool taken);
Addr pcPlus4 = pc + 4;
Addr targetAddr = case (iType)
J : {pcPlus4[31:28], imm[27:0]};
Jr : val;
Br : (taken? pcPlus4 + imm : pcPlus4);
Alu, Ld, St, Mfc0, Mtc0, Unsupported: pcPlus4;
endcase;
return targetAddr;
endfunction
Notes: 111

## Slide 112: Single-Cycle SMIPS
module [Module] mkProc(Proc);
Reg#(Addr) pc <- mkRegU;
RFile rf <- mkRFile;
IMemory iMem <- mkIMemory;
DMemory dMem <- mkDMemory;
Cop cop <- mkCop;
rule doProc(cop.started);
let inst = iMem.req(pc);
let dInst = decode(inst);
// trace - print the instruction
diplay("pc: %h inst: (%h) expanded: ", pc, inst, showInst(inst));
// read register values
let rVal1 = rf.rd1(validRegValue(dInst.src1));
let rVal2 = rf.rd2(validRegValue(dInst.src2));
Notes: 112

## Slide 113: Single-Cycle SMIPS atomic state updates
let eInst = exec(dInst, rVal1, rVal2, pc, ?, copVal); // The fifth argument is the predicted pc, to detect if it was mispredicted. Since there is no branch prediction, this field is sent with a random value
if(eInst.iType == Ld)
begin
let data <- dMem.req(MemReq{op: Ld, addr: eInst.addr, byteEn: ?, data: ?});
eInst.data = gatherLoad(eInst.addr, eInst.byteEn, eInst.unsignedLd, data);
end
else if(eInst.iType == St)
begin
match {.byteEn, .data} = scatterStore(eInst.addr, eInst.byteEn, eInst.data);
let d <- dMem.req(MemReq{op: St, addr: eInst.addr, byteEn: byteEn, data: data});
end
Notes: 113

## Slide 114: Single-Cycle SMIPS(2) atomic state updates
// write back
if(isValid(eInst.dst) && validValue(eInst.dst).regType == Normal)
rf.wr(validRegValue(eInst.dst), eInst.data);
// update the pc depending on whether the branch is taken or not
pc <= eInst.brTaken ? eInst.addr : pc + 4;
Notes: 114

## Slide 115: What Did We Learn?
SMIPS ISA
Full, single cycle implementation